## Slide 1
TRACK & FIELD MARKING
Dr. Rajan Bhatia

## Slide 2
RUNNING TRACK
2 Equal Straight & 2 Curves of equal radius
Straight
Curve
Curve
Straight

## Slide 3
Standard Track (400 m)
2 Equal Straights and 2 Curves of equal radius
Oval shape
Number of lanes 8
Length of the Straight = 84.39 m x 2 = 168.78 m
Length of the one Curve = 231.22 / 2 = 115.61m
Width of the lane = 1.22 m
Width of the line = 5 cm
Length of the track – length of the straights = total curve distance
400 – 168.78 = 231.22 m

## Slide 4: Now let us find out how to calculate curve radius?
r
231.22
(Running line radius)
m

## Slide 5
36.50 m
RUNNING LINE RADIUS.
115.61 meters
115.61 meters
RAISED BORDER 30 CM
Kerb Line ( Marking) RADIUS.
NON-RAISED BORDER
20 CM
36.80 m

## Slide 6
Inner Border Standard Track
Inner Border Non Standard Track
30 cm from Kerb line Radius
20 cm from Inner Border
Height of 0.05m to 0.065m and a width of 0.05m to 0.25m.

## Slide 7
36.50 m (CURVE RADIUS)
36.50 m (CURVE RADIUS)
9.76 m (1.22 x 8 lanes)
9.76 m (1.22 x 8 lanes)
5 m FREE SPACE
5 m FREE SPACE
102.5 m
REQUIRED AREA FOR 400 M OF 8 LANES TRACK WIDTH WISE

## Slide 8
36.50 m
36.50 m
84.39 m
9.76 m
9.76 m
5 m
5 m
REQUIRED AREA FOR 400 M TRACK OF 8 LANES LENGTH WISE
186.91 m

## Slide 9
105 m
190 m
STEP – 1. Measure the length and width of the given area

## Slide 10
Center point
STEP – 2. Find the center point of the given area by marking two diagonal lines from each corner of the field.
A
B
C
D
O

## Slide 11
10 M
42.195m
42.195 m
STEP – 3. Mark the straight line from the center point 42.195 meters towards each end.
o
A
B
C
D
E
F

## Slide 12
3M
4M
5M
STEP – 4. Mark the straight line making 90 degree angle at each end of the straight line.
F
E
H
I
J
H
K
L

## Slide 13
36.50 m
STEP – 5. Mark the curve by taking the (Kerb line radius) marking radius. i.e. 36.50 meters.
36.50 m

## Slide 14
36.50 m
O
Outer edge 36.50 m
Extension of tape from center to the kerb line radius

## Slide 15
36.50 m
STEP – 6. Join both ends of the two curve.
84.39 meters
84.39 meters
115.61 meters
115.61 meters

## Slide 16
37.72 m
36.50 m
STEP – 7. Increase the radius of curve by 1.22 meters and mark the second lane curve at both side and join the end of both the curves .

## Slide 17
Lane 1
Lane 2
Width of the lane
Inner border
1.22 m
1.22 m
Outer edge to outer edge

## Slide 18
37.72m
36.50 m
38.94 m
STEP – 8. Increase the radius again by 1.22 meters and mark the curve of third lane and join their ends by straight line.

## Slide 19
STEP – 9. Mark other lanes similarly as previous lanes have been marked by increasing 1.22 meters in the radius of the previous lane.

## Slide 20
STEP – 10. Extend the home straight for 100 meters and 110 meters run.
Line extended for 100 m/ 110 m H/ assembly line
FINISH

## Slide 21
Start Line
Finish Line
Width of the line is 5 cm
0.00 m
100 m
Running Direction

## Slide 22
Starts of 200 m. 400 m, 4 X 100 m Relay
For 400 m. Standard Track

## Slide 23
EVENT | STAGGER
200 M | ½ STAGGER
400 M | FULL STAGGER
4X100 M RELAY | FULL STAGGER
800 M | ½ STAGGER + DD
4X400 M RELAY | 1½ STAGGER +DD

## Slide 24
W = WIDTH OF THE LANE IN METRE
n = LANE NUMBER
FORMULA FOR CALCULATING FULL STAGGER
RAISED BORDERED TRACK
W (n-1) - 0.1 x 2π

## Slide 25
W = 1.22 m
n = Lane Number
= ((1.22(2-1)) - 0.1) x 2 x 3.1416
= (1.22 - 0.1) x 6.2832
= 1.12 x 6.2832
= 7.037 m
STAGGER FOR LANE No. 2
W (n-1) - 0.1 x 2π

## Slide 26
20 cm
STEP - 1
Extension of tape
7.037 m
Marking stagger

## Slide 27
7.04 m
14.71 m
22.38 m
Marking 400 meters staggers for lane 2. 3. and 4.
400 m start
o

## Slide 28
Distance running | Bends run in lanes | L2 | L3 | L4 | L5 | L6 | L7 | L8
200 M | 1 | 3.519 | 7.351 | 11.184 | 15.017 | 18.850 | 22.682 | 26.515
400 M | 2 | 7.037 | 14.703 | 22.368 | 30.034 | 37.699 | 45.365 | 53.030
800 M | 1 | 3.526 | 7.384 | 11.259 | 15.151 | 19.060 | 22.987 | 26.930
4 X 400 M | 3 | 10.563 | 22.086 | 33.627 | 45.185 | 56.760 | 68.352 | 79.960
STAGGER DISTANCES IN VARIOUS RACES IN STANDARD TRACK

## Slide 29
(W(n-1))X 2 
W = WIDTH OF THE LANE IN METERS
n = LANE NUMBER
FORMULA FOR CALCULATING FULL STAGGER
FOR NONBORDERED TRACK

## Slide 30
(W(n-1))X 2 
W = 1.22
n = Lane Number
= (1.22(2-1)) x 2 x 3.1416
= 1.22 x 6.2832
= 7.665 m
STAGGER FOR LANE No. 2
Keep on adding 7.67 m on the stagger of the previous lane you will get the next lane stagger

## Slide 31
Start for 800 m and 4 X 400 m Relay
For 800 m:- ½ Stagger + Diagonal Distance
For 4 X 400 m Relay:- 1½ Stagger + Diagonal Distance

## Slide 32
1.12 m
1.22 m
84.39 M
A
B
C
D
2.34m
Diagonal distance
BD²= AB² + AD²
BD²= (1.12)² + (84.39)²
BD=√1.2544 + 7121.6721
BD =84.3974
Diagonal Distance = BD - AD
DD= 84.3974 – 84.39
= .0074 m
CD²= AC² + AD²
CD =84.4224
DD= 84.4224 – 84.39
= .0324 m
Diagonal Distance = CD - AD
CD²= (2.34)² + (84.39)²
CD=√5.4756 + 7121.6721

## Slide 33
LANE NO. | DIAGONAL DISTANCE EXCESS
2 | 0.007 M
3 | 0.033 M
4 | 0.075 M
5 | 0.135 M
6 | 0.211 M
7 | 0.305 M
8 | 0.415 M

## Slide 34
84.39 M
A
B
BREAK LINE

## Slide 35
Placing cone just before the break line

## Slide 36
5 X 5 CM

## Slide 37
Marking of 1500 m start line

## Slide 38
30 cm
Step - 1

## Slide 39
A
B
AB =100 m
1500 M START LINE
C

## Slide 40
Starts of 3000 m, 5000 m, & 10000 m

## Slide 42
Radius of the Curved Start Line
Total curve distance divided by 8
Curve distance of lane 1 is 231.22 m
Radius of curve will be 231.22/8 = 28.90 m

## Slide 43
30 cm
STEP - 1

## Slide 44
28.90 Meters
Start line for 10000 m race
A
B
C
STEP - 2

## Slide 45
80 cm
80 cm
80 cm
15 cm
Blue (4X400 m Relay common Takeover zone)
Blue (4X400 m Relay first Takeover zone )
Various type of markings and their colour
End of takeover zone
Start of takeover zone
Inner border
Running Direction

## Slide 46
110 cm
110 cm
15 cm
Green (Break line)
Yellow (4X100 m Relay Takeover zone)
Green (400 m Hurdles)
10 cm
12.5 cm X12.5 cm
Blue (Steeplechase Hurdle)
End of Takeover zone
Start of Takeover zone

## Slide 47
4X100 m 2nd runner Scratch Line
Break line
400 m Hurdles
4X100 m
Takeover zone
Steeplechase Hurdle

## Slide 48
400 m Hurdles
100 m Hurdles
110 m Hurdle
Hurdles Marking and their colour

## Slide 49
SHOT PUT/ HAMMER / DISCUS THROW SECTOR

## Slide 50
DRAW A CIRCLE WITH THE RADIUS OF 1.0675 / 1.25 MTS.
1.0675 M/ 1.25 M
O

## Slide 51
MARK 19.07 MTS POINT FROM THE CENTRE OF THE CIRCLE TOWARDS THROWING DIRECTION
OA = 19.07MTS
O
A
4 m
B
5 M
3 M
5 M
3 M
E
F

## Slide 52
OA = 19.07MTS
O
A
B
E
F

## Slide 53
OA = 19.07MTS
O
A
FRONT HALF
5 CM

## Slide 54
OA = 19.07MTS
O
A
B
C
6 MTS
6 MTS
OB = 20 MTS
OC = 20 MTS

## Slide 55
O
34.92⁰
5 CM
5 CM
75 CM

## Slide 56
34.92⁰
1.20 – 1.22 M
30 CM
11.2 CM
STOP BOARD ONLY FOR SHOT PUT

## Slide 57
Marking
of
Javelin / Ball throw sector

## Slide 58
Reference Point
A
B
Draw a line AB of 4 meters with the help of reference Point
4 m
F
E
3 m
3 m
5 m
5 m
Javelin Marking

## Slide 59
4 m
8 m
4 m
28.96°
General competition 30 m
International competition 33.50 m and it can be kept 36.50 m also
75 cm
7 cm
Javelin Marking
75 cm
4 m
O
A
B
C
D
G
H
F
E
5 cm

## Slide 60
20 m
20 m
10 m
Rm/2
30 m
15 m
30 m
0
Javelin Marking

## Slide 61
THANKS FOR THE PATIENCE YOU SHOWED